# Stability Analysis of FLC

The stability for the design of FLC is a very important issue as it is used for control in the real world. Thus, there are always noise, disturbance, etc. The guarantee of stability of the system assures the usefulness in the real world.

However, in the current stage, there still need more research on this topic.

In fact, most published FLC systems could not provide a convicted analysis about the stability issue, but only presented the superior performance under given situations.

Then, whether the system is stable and whether it will be superior in another situation are left unspecified and difficult to assert.

# Stability Analysis of FLC

The lack of analysis for the stability of FLC arises from the difficulty in modeling the transition between rules.

Only the stability of individual rules cannot guarantee the stability of the whole system under the fuzzy inference.

Consider the following discrete fuzzy control system,

: IF x(k-1) is  THEN x(k+1)= x(k) – 0.5 x(k-1);

: IF x(k-1) is  THEN x(k+1)= - x(k) – 0.5 x(k-1);

where the membership functions of  and  are shown in the figure:

# Stability Analysis of FLC

It is easy to verify that the individual systems are stable. The response is shown as follows:

# Stability Analysis of FLC

But the response of the whole system is unstable:

If the membership function is changed as:

The response becomes:

# Stability Analysis of FLC

Consider the following fuzzy control system (zero input):

: IF x(k) is  AND … AND x(k-n+1) is  THEN

x(k+1)=x(k)+ … +x(k-n+1);

Or in state forms, the consequence is X(k+1)=X(k),

where X(k)= ,  =.

# Stability Analysis of FLC

The output of the fuzzy system is obtained as: X(k+1)=, where  is the fire strength of the i-th rule and l is the rule number.

Note that the multiple input variables are taken into account by product operations in this proof.

Consider the Lyapunov stability theorem; i.e., if a Lyapunov function, which is an energy type of functions and its derivative is always negative, then the system is said to be asymptotically stable in the large.

# Stability Analysis of FLC

Consider the following discrete fuzzy control system,

: IF x(k) is  and x(k-1) is  THEN x(k+1)= x(k) ;

: IF x(k) is  and x(k-1) is  THEN x(k+1)= x(k) ;

: IF x(k) is  and x(k-1) is  THEN x(k+1)= x(k) ;

where ==, and =.

The equilibrium of a fuzzy system is global asymptotically stable if there exists a common positive definite matrix P for all the systems such that <0 for all i.

# Stability Analysis of FLC

Pick P=.

It is easy to verify that <0 and <0.

However, it may be difficult to find such a matrix to suit all subsystems.

Note that even if there does not exist a common positive definite matrix P, the fuzzy system may be globally asymptotically stable.

# Stability Analysis of FLC

Let  be stable and nonsingular matrix for all i. Then, if there exists a common positive-definite matrix P such that <0 for all i then  is a stable matrix for all i and j.

In other words, if one of  is not a stable matrix, then there does not exist a common positive-definite matrix P such that <0.

Let P be a positive-definite matrix. If <0 for i=1, … , l, then <0 where  satisfies = where =1 and

# Stability Analysis of FLC

Common P is an approach to verify the stability.

To find such a matrix that satisfies some linear inequalities (positive definite) is called LMI (Linear Matrix Inequalities).

There is a Matlab toolbox can be used to solve LMI.

But, it is solved in a trial-and-error style. Thus, no solution found by the toolbox does not mean there is no solution for the considered LMI. Sometimes, by using different initial values may have different results.

How to use this approach for control design?

# Control Design for Fuzzy Systems

A common approach is Parallel Distributed Control (PDC).

PDC is to find controller for each rule individually.

Consider the i-th rule:

: IF x(k) is  AND … AND x(k-n+1) is  THEN

X(k+1)=X(k)+ Biui

If the state feedback is considered, ui= ( ki X(k)

Then, X(k+1)=(( ki Bi)X(k) =X(k) ( The remaining is the same.

# Control Design for Fuzzy Systems

Then we can still use the idea of common P to test the stability.

But, how to design not in a trial-and-error fashion?

Try to consider those feedback gains k’s and P as unknown parameters.

But, the inequalities are not linear (bilinear). ( (( ki Bi)P

Some approaches may be used to transform BMI to LMI. (try to define PK=M, P(1=W, Schur complement, etc.)

Note that such a transformation is conservative.

# Control Design for Fuzzy Systems

You can find a lot of such approaches in designing controller for fuzzy systems under various conditions (such as with uncertainties, delays, or with observer, etc.) in the literature.

Since those approaches are very conservative, there are also studies that try to find relax conditions for those approaches, like common P, solving LMI, or transferring BMI to LMI.

Another idea for designing controllers for a fuzzy system is to define a nominal system, which is a linear system, and then treat all rules as uncertainties. Then, the control design becomes robust control design.

Actually, some researchers also this idea to analyze properties of a fuzzy control system.